## Slide 1: Design of Digital Circuits Reading: Binary Numbers
Required Reading
for Week 1
20-21 February 2020
Spring 2020

## Slide 2: Binary Numbers

## Slide 3: In This Lecture
How to express numbers using only 1s and 0s
Using hexadecimal numbers to express binary numbers
Different systems to express negative numbers
Adding and subtracting with binary numbers

## Slide 4: Number Systems
Decimal Numbers
Binary Numbers

## Slide 5: Number Systems
Decimal Numbers
Binary Numbers

## Slide 6: Powers of two
20 | = |  |  | 28 | = | 
21 | = |  |  | 29 | = | 
22 | = |  |  | 210 | = | 
23 | = |  |  | 211 | = | 
24 | = |  |  | 212 | = | 
25 | = |  |  | 213 | = | 
26 | = |  |  | 214 | = | 
27 | = |  |  | 215 | = | 

## Slide 7: Powers of two
20 | = | 1 |  | 28 | = | 256
21 | = | 2 |  | 29 | = | 512
22 | = | 4 |  | 210 | = | 1024
23 | = | 8 |  | 211 | = | 2048
24 | = | 16 |  | 212 | = | 4096
25 | = | 32 |  | 213 | = | 8192
26 | = | 64 |  | 214 | = | 16384
27 | = | 128 |  | 215 | = | 32768
Handy to memorize up to 215

## Slide 8: Binary to Decimal Conversion
Convert 100112 to decimal

## Slide 9: Binary to Decimal Conversion
Convert 100112 to decimal
24 × 1 + 23 × 0 + 22 × 0 + 21 × 1 + 20 × 1 =

## Slide 10: Binary to Decimal Conversion
Convert 100112 to decimal
24 × 1 + 23 × 0 + 22 × 0 + 21 × 1 + 20 × 1 =
16 × 1 + 8 × 0 + 4 × 0 + 2 × 1 + 1 × 1 =
16 + 0 + 0 + 2 + 1 = 1910

## Slide 11: Decimal to Binary Conversion
Convert 4710 to binary

## Slide 12: Decimal to Binary Conversion
Convert 4710 to binary
  Start with 26 = 64 is 64 ≤ 47 ? no do nothing
  Now 25 = 32

## Slide 13: Decimal to Binary Conversion
Convert 4710 to binary
  Start with 26 = 64 is 64 ≤ 47 ? no do nothing
  Now 25 = 32 is 32 ≤ 47 ? yes subtract 47 – 32 =15
  Now 24= 16 is 16 ≤ 15 ? no do nothing
  Now 23= 8 is 8 ≤ 15 ? yes subtract 15 – 8 = 7
  Now 22= 4 is 4 ≤ 7 ? yes subtract 7-4 = 3
  Now 21= 2 is 2 ≤ 3 ? yes subtract 3-2 =1
  Now 20= 1 is 1 ≤ 1 ? yes we are done

## Slide 14: Decimal to binary conversion
Convert 4710 to binary
  Start with 26 = 64 is 64 ≤ 47 ? no 0 do nothing
  Now 25 = 32 is 32 ≤ 47 ? yes 1 subtract 47 – 32 =15
  Now 24= 16 is 16 ≤ 15 ? no 0 do nothing
  Now 23= 8 is 8 ≤ 15 ? yes 1 subtract 15 – 8 = 7
  Now 22= 4 is 4 ≤ 7 ? yes 1 subtract 7-4 = 3
  Now 21= 2 is 2 ≤ 3 ? yes 1 subtract 3-2 =1
  Now 20= 1 is 1 ≤ 1 ? yes 1 we are done
Result is 01011112

## Slide 15: Binary Values and Range
N-digit decimal number
  How many values?
  Range?
  Example: 3-digit decimal number
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values?
  Range:
  Example: 3-digit binary number
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
10N
  [0, 10N - 1]
2N
  [0, 2N - 1]

## Slide 16: Hexadecimal (Base-16) Numbers
Decimal | Hexadecimal | Binary
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
8 |  | 
9 |  | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
15 |  | 

## Slide 17: Hexadecimal (Base-16) Numbers
Decimal | Hexadecimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 18: Hexadecimal Numbers
Binary numbers can be pretty long.
A neat trick is to use base 16
How many binary digits represent a hexadecimal digit?
Example 32 bit number:
  0101 1101 0111 0001 1001 1111 1010 0110
4 (since 24 = 16)

## Slide 19: Hexadecimal Numbers
Binary numbers can be pretty long.
A neat trick is to use base 16
How many binary digits represent a hexadecimal digit?
Example 32 bit number:
  0101 1101 0111 0001 1001 1111 1010 0110 5 D 7 1 9 F A 6
4 (since 24 = 16)

## Slide 20: Hexadecimal Numbers
Binary numbers can be pretty long.
A neat trick is to use base 16
How many binary digits represent a hexadecimal digit?
Example 32 bit number:
  0101 1101 0111 0001 1001 1111 1010 0110 5 D 7 1 9 F A 6
The other way is just as simple
  C E 2 8 3 5 4 B
4 (since 24 = 16)

## Slide 21: Hexadecimal Numbers
Binary numbers can be pretty long.
A neat trick is to use base 16
How many binary digits represent a hexadecimal digit?
Example 32 bit number:
  0101 1101 0111 0001 1001 1111 1010 0110 5 D 7 1 9 F A 6
The other way is just as simple
  C E 2 8 3 5 4 B
  1100 1110 0010 1000 0011 0101 0100 1011
4 (since 24 = 16)

## Slide 22: Hexadecimal to Decimal Conversion
Convert 4AF16 (or 0x4AF) to decimal

## Slide 23: Hexadecimal to decimal conversion
Convert 4AF16 (or 0x4AF) to decimal
162 × 4 + 161 × A + 160 × F =
256 × 4 + 16 × 10 + 1 × 15 =
1024 + 160 + 15 = 119910

## Slide 24: Bits, Bytes, Nibbles…

## Slide 25: Powers of Two
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)

## Slide 26: Powers of Two (SI Compatible)
210 = 1 kibi ≈ 1000 (1024)
220 = 1 mebi ≈ 1 million (1,048,576)
230 = 1 gibi ≈ 1 billion (1,073,741,824)

## Slide 27: Estimating Powers of Two
What is the value of 224?
How many values can a 32-bit variable represent?

## Slide 28: Estimating Powers of Two
What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion

## Slide 29: Addition
Decimal
Binary

## Slide 30: Add the Following Numbers

## Slide 31: Add the Following Numbers
OVERFLOW !

## Slide 32: Overflow
Digital systems operate on a fixed number of bits
Addition overflows when the result is too big to fit in the available number of bits
See previous example of 11 + 6

## Slide 33: Overflow (Is It a Problem?)
Possible faults
Security issues

## Slide 34: Binary Values and Range
N-digit decimal number
  How many values?
  Range?
  Example: 3-digit decimal number
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values?
  Range:
  Example: 3-digit binary number
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
10N
  [0, 10N - 1]
2N
  [0, 2N - 1]

## Slide 35: Signed Binary Numbers
Sign/Magnitude Numbers
One’s Complement Numbers
Two’s Complement Numbers

## Slide 36: Sign/Magnitude Numbers
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
  +6 =
  - 6 =
Range of an N-bit sign/magnitude number:

## Slide 37: Sign/Magnitude Numbers
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
  +6 = 0110
  - 6 = 1110
Range of an N-bit sign/magnitude number:
  [-(2N-1-1), 2N-1-1]

## Slide 38: Problems of Sign/Magnitude Numbers
Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 wrong!
Two representations of 0 (± 0):
  1000
  0000
Introduces complexity in the processor design (Was still used by some early IBM computers)

## Slide 39: One’s Complement
A negative number is formed by reversing the bits of the positive number (MSB still indicates the sign of the integer):
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 |  | One’s Complement | Unsigned
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | = | +0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | = | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | = | 2 | 2
… | … | … | … | … | … | … | … |  | … | …
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | = | 127 | 127
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | = | -127 | 128
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | = | -126 | 129
… | … | … | … | … | … | … | … |  | … | …
1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | = | -2 | 253
1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | = | -1 | 254
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | = | -0 | 255

## Slide 40: One’s Complement
A negative number is formed by reversing the bits of the positive number (MSB still indicates the sign of the integer):
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 |  | One’s Complement | Unsigned
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | = | +0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | = | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | = | 2 | 2
… | … | … | … | … | … | … | … |  | … | …
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | = | 127 | 127
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | = | -127 | 128
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | = | -126 | 129
… | … | … | … | … | … | … | … |  | … | …
1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | = | -2 | 253
1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | = | -1 | 254
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | = | -0 | 255

## Slide 41: One’s Complement
The range of n-bit one’s complement numbers is: [-2n-1-1, 2n-1-1] 8 bits: [-127,127]
Addition:
  Addition of signed numbers in one's complement is performed using binary addition with end-around carry. If there is a carry out of the most significant bit of the sum, this bit must be added to the least significant bit of the sum:
Example: 17 + (-8) in 8-bit one’s complement
  0001 0001 (17)
  + 1111 0111 (-8)
  1 0000 1000
  + 1
  0000 1001 = (9)

## Slide 42: Two’s Complement Numbers
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Has advantages over one’s complement:
  Has a single zero representation
  Eliminates the end-around carry operation required in one's complement addition

## Slide 43: Two’s Complement Numbers
A negative number is formed by reversing the bits of the positive number (MSB still indicates the sign of the integer) and adding 1:
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 |  | Two’s Complement | Unsigned
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | = | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | = | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | = | 2 | 2
… | … | … | … | … | … | … | … |  | … | …
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | = | 127 | 127
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | = | -255 | 128
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | = | -254 | 129
… | … | … | … | … | … | … | … |  | … | …
1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | = | -3 | 253
1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | = | -2 | 254
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | = | -1 | 255

## Slide 44: Two’s Complement Numbers
A negative number is formed by reversing the bits of the positive number (MSB still indicates the sign of the integer) and adding 1:
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 |  | Two’s Complement | Unsigned
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | = | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | = | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | = | 2 | 2
… | … | … | … | … | … | … | … |  | … | …
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | = | 127 | 127
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | = | -128 | 128
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | = | -127 | 129
… | … | … | … | … | … | … | … |  | … | …
1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | = | -3 | 253
1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | = | -2 | 254
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | = | -1 | 255

## Slide 45: Two’s Complement Numbers
Same as unsigned binary, but the most significant bit (msb) has value of -2N-1
  Most positive 4-bit number:
  Most negative 4-bit number:
The most significant bit still indicates the sign (1 = negative, 0 = positive)
Range of an N-bit two’s comp number:
I = ∑ bi2i – bn-12n-1
i=0
i=n-2

## Slide 46: Two’s Complement Numbers
Same as unsigned binary, but the most significant bit (msb) has value of -2N-1
  Most positive 4-bit number: 0111
  Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
Range of an N-bit two’s comp number:
[-2N-1, 2N-1-1] 8 bits: [-128,127]
I = ∑ bi2i – bn-12n-1
i=0
i=n-2

## Slide 47: “Taking the Two’s Complement”
How to flip the sign of a two’s complement number:
  Invert the bits
  Add one
Example: Flip the sign of 310 = 00112

## Slide 48: “Taking the Two’s Complement”
How to flip the sign of a two’s complement number:
  Invert the bits
  Add one
Example: Flip the sign of 310 = 00112
  Invert the bits 11002

## Slide 49: “Taking the Two’s Complement”
How to flip the sign of a two’s complement number:
  Invert the bits
  Add one
Example: Flip the sign of 310 = 00112
  Invert the bits 11002
  Add one 11012

## Slide 50: “Taking the Two’s Complement”
How to flip the sign of a two’s complement number:
  Invert the bits
  Add one
Example: Flip the sign of 310 = 00112
  Invert the bits 11002
  Add one 11012
Example: Flip the sign of -810 = 110002

## Slide 51: “Taking the Two’s Complement”
How to flip the sign of a two’s complement number:
  Invert the bits
  Add one
Example: Flip the sign of 310 = 00112
  Invert the bits 11002
  Add one 11012
Example: Flip the sign of -810 = 110002
  Invert the bits 001112
  Add one 010002

## Slide 52: Two’s Complement Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers

## Slide 53: Two’s Complement Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Correct results if overflow bit is ignored

## Slide 54: Increasing Bit Width
A value can be extended from N bits to M bits (where M > N) by using:
  Sign-extension
  Zero-extension

## Slide 55: Sign-Extension
Sign bit is copied into most significant bits
Number value remains the same
Give correct result for two’s complement numbers
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011

## Slide 56: Zero-Extension
Zeros are copied into most significant bits
Value will change for negative numbers
Example 1:
  4-bit value = 00112 = 310
  8-bit zero-extended value: 000000112 = 310
Example 2:
  4-bit value = 10112 = -510
  8-bit zero-extended value: 000010112 = 1110

## Slide 57: Number System Comparison
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:

## Slide 58: Lessons Learned
How to express decimal numbers using only 1s and 0s
How to simplify writing binary numbers in hexadecimal
Adding binary numbers
Methods to express negative numbers
  Sign Magnitude
  One’s complement
  Two’s complement (the one commonly used)